## Slide 1
R.M.S. – “Root Mean Square”
A mathematical trick to help our calculations behave like the real world
Consider the molecules in a gas
They’re all moving in different directions, randomly.
So their average velocity is zero.
Even if we heat the gas so they move faster, the average velocity is still zero.

## Slide 2
The a.c. voltage is going up and down, positive & negative, 50 times each second.
So the average voltage is zero.
So if you grab hold of that live wire, you’ll be fine, right?
Consider the live wire in a UK mains flex.
We need a way to deal with these situations that doesn’t give us a zero result.
It’s called a “root mean square”

## Slide 3
The a.c. mains example is the easiest one to learn about first.
Here’s the waveform

## Slide 4
First, we square it.
Now it’s all positive

## Slide 5
First, we square it.
Now it’s all positive
THEN we take the mean 

## Slide 6
Then we take the square root 
The green line is the Root of the Mean of the SQUARE of the original waveform
Calculating it is quite a bit of work.
But for a sine wave there’s a short cut: Vrms = Vpeak/
Or Vrms = 0.7071 x Vpeak
An a.c. voltmeter gives you the rms voltage, not the peak.
That’s handy – because the power transferred e.g. in a heater is calculated using the rms voltage
What you’ve believed to be 230V a.c UK mains is actually 325V peak voltage